## Slide 1
Proyecto Final de Grado Ingeniería en la Edificación modalidad de intercambio académico curso 20011-12
United Kingdom/Loughborough
Alumno: Paula Cosar Jorda
tutor destino: Richard Buswell
tutor ETSGE: Isabel Tort Ausina
Energy efficiency in UK residential buildings
“Low effort energy demand reduction”
Electricity Incomes
Distribution Circuits
Reading electricity consumption within a real house:
Energy use in dwellings (UK,2008) accounted for nearly 30% of the total energy demand. How, when and what for is used the energy at sample households? What percentage is caused by the cooker? What is caused by lighting? Is there any trend followed by the dwelling? How can we get further reductions in electricity consumption?
2% Lighting
The lights upstairs are fully equipped with CFL, the power demand is so low that is not picked up by the electric meter. Downstairs lights are a mixture of CFL and incandescent lights. Power loads are near 10 times the power upstairs.
Comparing with the other houses of study equipped with incandescent lights, they are saving about 90% of the electricity.
22% Utility
Washing machine £5/month
Tumble dryer £16/month
Dishwasher £11/month
8% Cooling
The electric shower is a powerful device. It is the top electricity consumer within the house.
Electric Shower £26/month
20% Personal Hygiene
15% Cookery
The main appliances in the kitchen are:
Cooker £7/month
Kettle: £1/month
*The kettle is the device used in England to warm water for Tea.
This family use it every 3 hours!
11% Entertainment
The standby position on TVs, gamers and Video records consume constant power very easy to avoid but depending on the householder decision.
3% Aquarium
*The estimation is done with two weeks of data. 13% of the electricity consumption measured in the main circuit is not picked up by the meters in the circuits.
4 laptops + 1 computer.
Computer power on standby position = 24W.
Power in use = 100 W.
The power for the most efficient laptop is around the power than is being use by the computer on standby.
6% Battery Chargers
It is programmed to keep the right temperature and conditions for fishes needs.
It costs less than £1/month
The fridge and the freezer show sparks when losing temp.
To avoid peaks in the electricity consumption is critical for the energy efficiency of those devices.
Freezer £7/month
Fridge £3/month
MJ
W
W
W
W
W
Feedback and Energy awareness:
To get further feedback in dwellings electricity consumption is need to understand which behaviours and lifestyles can drive to get a sustainable lifestyle and to create a global energy conscience.
Educational and political interventions might lead householders to understand the meaning of using their house appliances in terms of energy consumption. Clarify the difference between covering a need and having a luxury, alert about the energy used on standby position in most of the appliances, advise about powerful devices such as dryers or electric showers and motivating sustainable design for new devices.
The solar panel produced 20% of the Total electricity consumption!
Notes: 1
1