## Slide 1
Proyecto Final de Grado Ingeniería de Edificación modalidad de intercambio académico curso 2011-2012
LITUANIA / LITHUANIA – Vilna / Vilnius
Alumno: IGNACIO MARÍA VEGUER ALFONSO
tutor destino: JONAS SAPARAUSKAS
tutor ETSIE: BEGOÑA FUERTES GINER
Construction design of multi-dwelling building at Maudyklos str. In Vilnius / Poster Resumen PFG
ARQUITECHTURAL PART
Elniakampis apartment house is located in the forest on a quiet Elniakampis Street in a prestigious district of Vilnius – Valakampiai. A small three-storey 17-apartment house is
designed to let in the maximum amount of natural light. The layout of the apartments is both convenient (from 34,90 m2 to 140,20 m2) and practical. Each apartment comes with a box room, parking place under the house and economical gas heating. There is a possibility to install fireplaces in each apartment. A bus stop (No. 15) is just 200 m away from the house. Just a couple of kilometres away you would find Nemencine Road, leading you to the shopping center, Sauletekis University campus and Baltic-American Clinic that provides medical services 24 hours a day. All the infrastructure of Antakalnis district is nearby. Surfaces: - Building area: 671.47 m2 - Plot: 1200 m2
CONSTRUCTIONAL PART
In this part there is the calculation of one representative part of the roof slab of the building. Calculation and process are in thesisbook.
En esta parte es el cálculo de una parte representativa de la losa de cubierta del edificio. Los cálculos y procedimiento están en la memoria.
TECHNOLOGICAL CARDS
We are going to study the plasterboards of second floor. There are 70.7 m2 of normal
plasterboard and 25.93 m2 of waterproof plasterboard. Waterproof plasterboard will be in
wet zones such as bathrooms. Plasterboard partitions are composed of a metal frame and gypsum board screwed to each side. The metal frame is attached to the original construction and constitutes a support for mounting plates. For special cases you can use a double structure with adequate separation. In the gap between the plates can be placed a fiberglass or rock lada for greater thermal and acoustic insulation and for fire protection. Furthermore, in the gap can perform the necessary facilities (electric, sanitary etc.).
We study the ventilated facade with ceramic finish. The surface covered with this kind of facade is 290.46 m2. The ventilated facade is a design element consisting of two sheets, one outdoor and one indoor, which contain between them an air vented instructing the seal and protect from direct sunlight.
CONSTRUCTION MASTERPLAN
In the plan of building lot is intended:
The main machines working places and moving tracks, storages and storing sites positions, temporary electricity, water-supplying, sewerage and fireplug positions, safety and dangerous zones, temporary access roads and passages, temporary buildings positions. The plan of building lot is preparing before starting constructional works. The lot is on planning, trees, which are impeding, are cutting of, the soil is pushed aside and stored. All the site preparation has to be made according to construction organizing project. The building lot is surrounding by fence. The working zone of crane and dangerous zones are marked. On the preparation stage, it is necessary to do these works: To prepare temporary building for workers, to cut trees which are in the building zone, to make a entrance to work place and to prepare storage sites. All temporary buildings will be supplied by electricity. The building site will be supplied by electricity from the transformer substation, where is the main electricity distributional and accounting lock and cable. The bathroom temporary building will be supplied by water, and will need sanitary installation.
VILNIUS GEDIMINAS TECHNICAL
UNIVERSITY
FACULTY OF CIVIL ENGINEERING
Elniakampis casa de apartamentos está situado en el bosque en una calle tranquila Elniakampis en un prestigioso distrito de Vilnius - Valakampiai. Un pequeño edificio de tres pisos con 17 apartamentos diseñado para permitir la máxima cantidad de luz natural. La distribución de los apartamentos es muy cómoda (desde 34,90 m2 hasta 140,20 m2) y práctica. Todos los apartamentos cuentan con un trastero, plaza de garaje debajo de la casa y calefacción. Existe la posibilidad de instalar chimeneas en cada apartamento. Una parada de autobús (n º 15) está a 200 metros de la casa. Sólo un par de kilómetros de distancia se encontraría camino Nemencine, que le conduce al centro comercial, a la Universidad y a la Clínica del Báltico-estadounidense que ofrece servicios médicos las 24 horas del día. Toda la infraestructura del distrito de Antakalnis está cerca. Superficies: - Superficie de construcción: 671,47 m2 - Parcela: 1200 m2
Vamos a estudiar las placas de yeso laminado del segundo piso. Hay 70,7 m2 de yeso normal y 25,93 m2 de paneles de yeso hidrófugo. Placa de yeso hidrófuga estará en
zonas húmedas como baños. Particiones yeso están compuestas de una estructura metálica y tablero de yeso atornillado a cada lado. La estructura metálica está unida a la construcción original y constituye un soporte para las placas de montaje. Para casos especiales se puede utilizar una estructura doble con una separación adecuada. En el espacio entre las placas se puede colocar una fibra de vidrio o lana de roca para un mayor aislamiento térmico y acústico y protección contra incendios. Por otra parte, en la brecha puede llevar a cabo las instalaciones necesarias (eléctrica, sanitaria, etc.)
Se estudia la fachada ventilada con acabado cerámico. La superficie cubierta con este tipo de fachada es de 290,46 m2. La fachada ventilada es un elemento de diseño que consta de dos hojas, una exterior y otra interior, que contienen entre ellas una cámara de aire ventilada y protege de la luz solar directa y de las temperaturas extremas.
En el plan de construcción tiene por objeto:
Los lugares de trabajo de las máquinas principales, posicion de acopios, instalaciones provisionales y boca de incendios, seguridad y zonas peligrosas, caminos de acceso temporal y accesos, las posiciones de los edificios provisionales. Toda la preparación del terreno tiene que ser de acuerdo a proyecto y de la organización. El solar esttará vallado perimetralmente. La zona de trabajo de la grúa y el radio de seguridad están marcados. En la etapa de preparación, es necesario hacer estas obras: Preparar el edificio temporal para los trabajadores, cortar los árboles que se encuentran en la zona de construcción, para hacer un acceso rodado al lugar de trabajo y preparar los lugares de acopio.
Todos los edificios provisionales serán suministrados por electricidad. La obra será suministrada por la electricidad de la subestación transformadora, donde está la cerradura principal de electricidad de distribución y la contabilidad y el cable. La caseta de baño provisional estara dotada de instalación de agua, y será necesaria la instalación de aguas residuales.
Notes: 1
1