## Slide 1: REMOTE CONTROL OF A MECHATRONICS SYSTEM WITH WIRELESS COMMUNICATIONS
AUTHOR: BHARATH KUMAR MITTAPALLI
TUTOR : JUAN JOSÉ SERRANO MARTÍN

## Slide 2
INDEX
Purpose of the Project
Objectives
Study Flow
Our System – CNC Introduction
Block Diagram
Components
  STM32 F3 Discovery
  Telit LE-50 868
  Analog Joystick
Structure
Programming – Keil
Result

## Slide 3
Purpose of the project
Mechatronic Machine – CNC
Re-modelling
Upgradation
Remote Control

## Slide 4
OBJECTIVES
Develop the system by modifying the components.
Check in wired mode
Improve accuracy, stability and ease.
Include a Rf-Module for wireless mode.

## Slide 5
STUDY fLOW
Mechanical part of work
Electrical and Electronic connections
Study about our components
Configure the Microcontroller
Write the program
Get ready the Rf-module and joystick
Update the code
Check the functioning of the machine

## Slide 6
CNC SYSTEM
First cnc concept introduced by Professor John T. Parsons in early 1950’s
First cnc model designed in1953 by Professor John T. Parsons company along with US Airforce at MIT
Initially point-to-point movement. Later linear and Circular movements

## Slide 7
BLOCK DIAGRAM
STM 32 F3 Discovery Board
Microcontroller
Telit LE50-868
RF Module
Mechatronic System
Motor X
Motor Y
Limit Switches
12V Power Supply
Receiver End

## Slide 8
BLOCK DIAGRAM
STM 32 F3 Discovery Board
Microcontroller
Telit LE50-868
RF Module
Analog Joystick
PC
Or
Laptop
Transmission End

## Slide 9
COMPONENTS
32-bit MCU device
100 pin package
256 kB flash
48 kB RAM
LED’s, GPIO’s, timers, convertors, Usart channels, etc.

## Slide 10
CONFIGURATION WITH STM32CubeMX

## Slide 11
COMPONENTS
DC motor
Kelvin K30 37.62
Limit switch
Analog Joystick
Two analog inputs
One digital input

## Slide 12
Components
Telit LE50-868 Rf Module
Range up to 2000m
Flash up to 128 kB, RAM of 4 kB, EEPROM of 2 kB
4 timers, 32.768 kHz real time clock (RTC)
Excellent Receiver Sensitivity
9 I/O ports maximum available

## Slide 13
CONFIGURATION OF RF MODULE
Configure parameters using Telit SR Manager tool

## Slide 14
CONFIGURATION OF RF MODULE

## Slide 15
STRUCTURE
Receiver End

## Slide 16
STRUCTURE
Transmission End - Joystick

## Slide 17
PROGRAMMING - KEIL
Software development toolchain
Programming, compiling and debugging
Keil version 5

## Slide 18
RESULT
The movement of the motors of the machine is satisfactory
The rf module functions well in a good range
Transmission data can be viewed on the hyper-terminal
Limit switches are sensitive and taken care of
Motors are smooth running and good response
Future scope
Can be improvised to do in three axes (3D)
The rf module can be replaced by a wi-fi module
The end effector can be adapted as required in various fields.